## Slide 1: ENEE244-02xx Digital Logic Design
Lecture 10

## Slide 2: Announcements
HW4 assigned, due 10/9

## Slide 3: Agenda
Recap:
  The simplification problem (4.1)
This time:
  Prime Implicants (4.2)
  Prime Implicates (4.3)
  Karnaugh Maps (4.4)

## Slide 4: The Simplification Problem
The determination of Boolean expressions that satisfy some criterion of minimality is the simplification or minimization problem.
We will assume cost is determined by number of gate inputs.

## Slide 5: Prime Implicants
implies
  There is no assignment of values to the n variables that makes equal to 1 and equal to 0.
  Whenever equals 1, then must also equal 1.
  Whenever equals 0, then must also equal 0.
Concept can be applied to terms and formulas.

## Slide 6: Examples
Case of Disjunctive Normal Formula
  Sum-of-products form
  Each of the product terms implies the function being described by the formula
  Whenever product term has value 1, function must also have value 1.
Case of Conjunctive Normal Formula
  Product-of-sums form
  Each sum term is implied by the function
  Whenever the sum term has value 0, the function must also have value 0.

## Slide 7: Subsumes
A term is said to subsume a term iff all the literals of the term are also literals of the term .
Example:
If a product term subsumes a product term , then implies .
  Why?
If a sum term subsumes a sum term , then implies .
  Why?

## Slide 8: Subsumes
Theorem:
  If one term subsumes another in an expression, then the subsuming term can always be deleted from the expression without changing the function being described.
CNF:
DNF:

## Slide 9: Implicants and Prime Implicants
A product term is said to be an implicant of a complete function if the product term implies the function.
Each of the minterms in minterm canonical form is an implicant of the function.
An implicant of a function is a prime implicant if the implicant does not subsume any other implicant with fewer literals.

## Slide 10: Example
x | y | z | f
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
is an implicant. Is it a prime implicant?
is also an implicant
is an implicant.
Is it a prime implicant?
Yes. are not implicants

## Slide 11: Prime Implicants
Theorem:
  When the cost for a minimal Boolean formula is such that decreasing the number of literals in the DNF formula decreases the cost of the formula, the minimal DNFs correspond to sums of prime implicants.
Proof:
  Assume not. Then there is a DNF with minimal cost c that is not the sum of only prime implicants.
  Let be one such term in .
  So implies the function and subsumes some which implies the function.
  Add to the formula.
  Remove by the absorption law.
  New expression with same number of terms but fewer literals.
  This new expression has lower cost which contradicts minimality of

## Slide 12: Irredundant Disjunctive Normal Formulas
Definition: An expression in sum-of-products form such that:
  Every product term in the expression is a prime implicant
  No product term may be eliminated from the expression without changing the function described by the expression.
Theorem:
  When the cost of a formula decreases when a literal is removed, the minimal DNFs correspond to irredundant disjunctive normal formulas.

## Slide 13: Prime Implicates and Irredundant Conjunctive Expressions
A sum term is said to be an implicate of a complete function if the function implies the sum term.
Each of the maxterms in maxterm canonical form is an implicate of the function.
An implicate of a function is a prime implicate if the implicate does not subsume any other implicate with fewer literals.

## Slide 14: Example
x | y | z | f
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
is an implicate. Is it a prime implicate?
is also an implicant
is an implicate.
Is it a prime implicate?
Yes. are not implicates

## Slide 15: Prime Implicates
Theorem:
  When the cost for a minimal Boolean formula is such that decreasing the number of literals in the CNF formula decreases the cost of the formula, the minimal CNFs correspond to products of prime implicates.

## Slide 16: Irredundant Conjunctive Normal Formulas
Definition: An expression in product-of-sums form such that:
  Every sum term in the expression is a prime implicate
  No sum term may be eliminated from the expression without changing the function described by the expression.
Theorem:
  When the cost of a formula decreases when a literal is removed, the minimal CNFs correspond to irredundant conjunctive normal formulas.

## Slide 17: Karnaugh Maps
Method for graphically determining implicants and implicates of a Boolean function.
Simplify Boolean functions and their logic gates implementation.
Geometrical configuration of cells such that each of the -tuples corresponding to the row of a truth table uniquely locates a cell on the map.
The functional values assigned to the n-tuples are placed as entries in the cells.
Structure of Karnaugh map:
  Two cells are physically adjacent within the configuration iff their respective n-tuples differ in exactly one element.
  E.g. (0,1,1), (0,1,0)
  E.g. (1,0,1), (1,1,0)

## Slide 18: Three-Variable Maps
1 | 0 | 0 | 1
1 | 1 | 0 | 0
Each cell is adjacent to 3 other cells.
Imagine the map lying on the surface of a cylinder.
00
01
11
10
0
1

## Slide 19: Four-Variable Maps
1 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
Each cell is adjacent to 4 other cells.
Imagine the map lying on the surface of a torus.
00
01
11
10
00
01
11
10

## Slide 20: Karnaugh Maps and Canonical Formulas
Minterm Canonical Formula
1 | 0 | 0 | 1
1 | 1 | 0 | 0
00
01
11
10
0
1

## Slide 21: Karnaugh Maps and Canonical Formulas
Maxterm Canonical Formula
1 | 0 | 0 | 1
1 | 1 | 0 | 0
00
01
11
10
0
1

## Slide 22: Karnaugh Maps and Canonical Formulas
Decimal Representation
0 | 1 | 3 | 2
4 | 5 | 7 | 6
00
01
11
10
0
1

## Slide 23: Karnaugh Maps and Canonical Formulas
Decimal Representation
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
00
01
11
10
00
01
11
10

## Slide 24: Product Term Representations on Karnaugh Maps
Any set of 1-cells which form a rectangular grouping describes a product term with variables.
Rectangular groupings are referred to as subcubes.
The total number of cells in a subcube must be a power-of-two ().
Two adjacent 1-cells:

## Slide 25: Examples of Subcubes

## Slide 26: Subcubes for elimination of one variable
 | 1 | 1 | 
00
01
11
10
00
01
11
10
Product term:
Variables in the product term are variables whose value is constant inside the subcube.

## Slide 27: Subcubes for elimination of one variable
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 28: Subcubes for elimination of one variable
 |  | 1 | 
 |  | 1 | 
00
01
11
10
00
01
11
10
Product term:

## Slide 29: Subcubes for elimination of one variable
1 |  |  | 
1 |  |  | 
00
01
11
10
00
01
11
10
Product term:

## Slide 30: Subcubes for elimination of two variables
1 | 1 |  | 
1 | 1 |  | 
00
01
11
10
00
01
11
10
Product term:

## Slide 31: Subcubes for elimination of two variables
 |  | 1 | 
 |  | 1 | 
 |  | 1 | 
 |  | 1 | 
00
01
11
10
00
01
11
10
Product term:

## Slide 32: Subcubes for elimination of two variables
1 | 1 | 1 | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 33: Subcubes for elimination of two variables
1 |  |  | 1
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 34: Subcubes for elimination of two variables
1 |  |  | 1
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 35: Subcubes for elimination of three variables
1 | 1 | 1 | 1
1 | 1 | 1 | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 36: Subcubes for elimination of three variables
 | 1 | 1 | 
 | 1 | 1 | 
 | 1 | 1 | 
 | 1 | 1 | 
00
01
11
10
00
01
11
10
Product term:

## Slide 37: Subcubes for elimination of three variables
1 | 1 | 1 | 1
1 | 1 | 1 | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 38: Subcubes for elimination of three variables
1 |  |  | 1
1 |  |  | 1
1 |  |  | 1
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 39: Subcubes for sum terms
0 | 0 | 0 | 0
0 | 0 | 0 | 0
 |  | 0 | 0
0 | 0 | 0 | 0
00
01
11
10
00
01
11
10
Sum terms:

## Slide 40: Using K-Maps to Obtain Minimal Boolean Expressions

## Slide 41: Example
0 | 0 | 0 | 1
0 | 0 | 1 | 1
00
01
11
10
0
1
Both are prime implicants
How do we know this is minimal?

## Slide 42: Finding the set of all prime implicants in an n-variable map:
If all entries are 1, then function is equal to 1.
For i = 1, 2. . . n
  Search for all subcubes of dimensions that are not totally contained within a single previously obtained subcube.
  Each of these subcubes represents an variable product term which implies the function.
  Each product term is a prime implicant.

## Slide 43: Essential Prime Implicants
Some 1-cells appear in only one prime implicant subcube, others appear in more than one.
A 1-cell that can be in only one prime implicant is called an essential prime implicant.
1 | 1 | 0 | 0
0 | 1 | 1 | 0
00
01
11
10
0
1

## Slide 44: Essential Prime Implicants
Every essential prime implicant must appear in all the irredundant disjunctive normal formulas of the function.
Hence must also appear in a minimal sum.
  Why?

## Slide 45: General Approach for Finding Minimal Sums