## Slide 1: ENEE244-02xx Digital Logic Design
Lecture 10

## Slide 2: Announcements
HW4 due 10/9
  Please omit last problem 4.6(a),(c)
Quiz during recitation on Monday (10/13)
  Will cover material from lectures 10,11,12.

## Slide 3: Agenda
Last time:
  Prime Implicants (4.2)
  Prime Implicates (4.3)
This time:
  Karnaugh Maps (4.4)

## Slide 4: Karnaugh Maps
Method for graphically determining implicants and implicates of a Boolean function.
Simplify Boolean functions and their logic gates implementation.
Geometrical configuration of cells such that each of the -tuples corresponding to the row of a truth table uniquely locates a cell on the map.
The functional values assigned to the n-tuples are placed as entries in the cells.
Structure of Karnaugh map:
  Two cells are physically adjacent within the configuration iff their respective n-tuples differ in exactly one element.
  E.g. (0,1,1), (0,1,0)
  E.g. (1,0,1), (1,1,0)

## Slide 5: Three-Variable Maps
1 | 0 | 0 | 1
1 | 1 | 0 | 0
Each cell is adjacent to 3 other cells.
Imagine the map lying on the surface of a cylinder.
00
01
11
10
0
1

## Slide 6: Four-Variable Maps
1 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
Each cell is adjacent to 4 other cells.
Imagine the map lying on the surface of a torus.
00
01
11
10
00
01
11
10

## Slide 7: Karnaugh Maps and Canonical Formulas
Minterm Canonical Formula
1 | 0 | 0 | 1
1 | 1 | 0 | 0
00
01
11
10
0
1

## Slide 8: Karnaugh Maps and Canonical Formulas
Maxterm Canonical Formula
1 | 0 | 0 | 1
1 | 1 | 0 | 0
00
01
11
10
0
1

## Slide 9: Karnaugh Maps and Canonical Formulas
Decimal Representation
0 | 1 | 3 | 2
4 | 5 | 7 | 6
00
01
11
10
0
1

## Slide 10: Karnaugh Maps and Canonical Formulas
Decimal Representation
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
00
01
11
10
00
01
11
10

## Slide 11: Product Term Representations on Karnaugh Maps
Any set of 1-cells which form a rectangular grouping describes a product term with variables.
Rectangular groupings are referred to as subcubes.
The total number of cells in a subcube must be a power-of-two ().
Two adjacent 1-cells:

## Slide 12: Examples of Subcubes

## Slide 13: Subcubes for elimination of one variable
 | 1 | 1 | 
00
01
11
10
00
01
11
10
Product term:
Variables in the product term are variables whose value is constant inside the subcube.

## Slide 14: Subcubes for elimination of one variable
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 15: Subcubes for elimination of one variable
 |  | 1 | 
 |  | 1 | 
00
01
11
10
00
01
11
10
Product term:

## Slide 16: Subcubes for elimination of one variable
1 |  |  | 
1 |  |  | 
00
01
11
10
00
01
11
10
Product term:

## Slide 17: Subcubes for elimination of two variables
1 | 1 |  | 
1 | 1 |  | 
00
01
11
10
00
01
11
10
Product term:

## Slide 18: Subcubes for elimination of two variables
 |  | 1 | 
 |  | 1 | 
 |  | 1 | 
 |  | 1 | 
00
01
11
10
00
01
11
10
Product term:

## Slide 19: Subcubes for elimination of two variables
1 | 1 | 1 | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 20: Subcubes for elimination of two variables
1 |  |  | 1
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 21: Subcubes for elimination of two variables
1 |  |  | 1
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 22: Subcubes for elimination of three variables
1 | 1 | 1 | 1
1 | 1 | 1 | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 23: Subcubes for elimination of three variables
 | 1 | 1 | 
 | 1 | 1 | 
 | 1 | 1 | 
 | 1 | 1 | 
00
01
11
10
00
01
11
10
Product term:

## Slide 24: Subcubes for elimination of three variables
1 | 1 | 1 | 1
1 | 1 | 1 | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 25: Subcubes for elimination of three variables
1 |  |  | 1
1 |  |  | 1
1 |  |  | 1
1 |  |  | 1
00
01
11
10
00
01
11
10
Product term:

## Slide 26: Subcubes for sum terms
0 | 0 | 0 | 0
0 | 0 | 0 | 0
 |  | 0 | 0
0 | 0 | 0 | 0
00
01
11
10
00
01
11
10
Sum terms:

## Slide 27: Using K-Maps to Obtain Minimal Boolean Expressions

## Slide 28: Example
0 | 0 | 0 | 1
0 | 0 | 1 | 1
00
01
11
10
0
1
Both are prime implicants
How do we know this is minimal?
Need an algorithmic procedure.

## Slide 29: Finding the set of all prime implicants in an n-variable map:
If all entries are 1, then function is equal to 1.
For i = 1, 2. . . n
  Search for all subcubes of dimensions that are not totally contained within a single previously obtained subcube.
  Each of these subcubes represents an variable product term which implies the function.
  Each product term is a prime implicant.

## Slide 30: Finding the set of all prime implicants
1 | 1 | 0 | 1
1 | 1 | 0 | 1
0 | 0 | 0 | 1
1 | 0 | 0 | 1
00
01
11
10
00
01
11
10
Subcubes consisting of 16 cells—None
Subcubes consisting of 8 cells—None
Subcubes consisting of 4 cells in blue.
Subcubes consisting of 2 cells in red (not contained in another subcube).
Subcubes consisting of 1 cell (not contained in another subcube)—None.

## Slide 31: Essential Prime Implicants
Some 1-cells appear in only one prime implicant subcube, others appear in more than one.
A 1-cell that can be in only one prime implicant is called an essential prime implicant.
1 | 1 | 0 | 0
0 | 1 | 1 | 0
00
01
11
10
0
1

## Slide 32: Essential Prime Implicants
Every essential prime implicant must appear in all the irredundant disjunctive normal formulas of the function.
Hence must also appear in a minimal sum.
  Why?

## Slide 33: General Approach for Finding Minimal Sums
Find all prime implicants using K-map
Find all essential prime implicants using K-map
**If all 1-cells are not yet covered, determine optimal choice of remaining prime implicants using K-map.

## Slide 34: Next time: Lots of examples of finding minimal sums using K-maps