## Slide 1: ENEE244-02xx Digital Logic Design
Lecture 7

## Slide 2: Announcements
Homework 3 due on Thursday.
Review session will be held by Shang during class on Thursday.
Midterm on Tuesday, Sept. 30.

## Slide 3: First Exam
8 questions, some with multiple parts
Will cover material from Lectures 1-7
Including (list on course webpage):
  Positional number systems: basic arithmetic, polynomial and iterative methods of number conversion, special conversion procedures.
  Signed numbers and complements: r's complement, (r-1)'s complement, addition and subtraction using r's complement, (r-1)'s complement.
  Codes: Error detection, error correction, parity check code, Hamming code.
  Boolean Algebra: definition, postulates, theorems, principle of duality.
  Boolean formulas and functions: canonical formulas, minterm canonical formulas, maxterm canonical formulas, m-Notation, M-notation, manipulation and simplification of Boolean formulas
  Gates and combinational networks: various types of gates, universal gates, synthesis procedure, Nand and Nor gate realizations.
  Incomplete Boolean functions and don't care conditions: truth table representation, satisfiability don't cares, observability don't cares.
  Gate properties: noise margins, fan-out, propagation delays, power dissipation.

## Slide 4: Agenda
Last time:
  Universal Gates (3.9.3)
  NAND/NOR/XOR Gate Realizations (3.9.4-3.9.6)
  Gate Properties (3.10)
This time:
  Some examples of Synthesis Procedure
  The simplification problem (4.1)
  Prime Implicants (4.2)
  Prime Implicates (4.3)

## Slide 5: Synthesis Procedure Examples

## Slide 6: Synthesis Procedure
High-level description: A function with finite domain and range.
Binary-level: All input-output variables are binary.

## Slide 11: Simplification of Boolean Expressions

## Slide 12: Formulation of the Simplification Problem
What evaluation factors for a logic network should be considered?
  Cost (of components, design, construction, maintenance)
  Reliability (highly reliable components, redundancy)
  Time it takes for network to respond to changes at its inputs.

## Slide 13: Minimal Response Time
Achieved by minimizing the number of levels of logic that a signal must pass through.
Always possible to construct any logic network with at most two levels under the double-rail logic assumption.
  Why?

## Slide 14: Minimal Component Cost
Assume this is the only other factor influencing the merit evaluation of a logic network.
In general, there are many two-level realizations.
Determine the normal formula with minimal component cost.
Number of gates is one greater than the number of terms with more than one literal in the expression.
Number of gate inputs is equal to the number of literals in the expression plus the number of terms containing more than one literal.
Using these criteria can obtain a measure of a Boolean expression’s complexity called the cost of the expression.

## Slide 15: The Simplification Problem
The determination of Boolean expressions that satisfy some criterion of minimality is the simplification or minimization problem.
We will assume cost is determined by number of gate inputs.

## Slide 16: Fundamental Terms
A product or sum of literals in which no variable appears more than once.
Can obtain a fundamental term by noting:

## Slide 17: Prime Implicants
implies
  There is no assignment of values to the n variables that makes equal to 1 and equal to 0.
  Whenever equals 1, then must also equal 1.
  Whenever equals 0, then must also equal 0.
Concept can be applied to terms and formulas.

## Slide 18: Examples

## Slide 19: Examples
Case of Disjunctive Normal Formula
  Sum-of-products form
  Each of the product terms implies the function being described by the formula
  Whenever product term has value 1, function must also have value 1.
Case of Conjunctive Normal Formula
  Product-of-sums form
  Each sum term is implied by the function
  Whenever the sum term has value 0, the function must also have value 0.

## Slide 20: Subsumes
A term is said to subsume a term iff all the literals of the term are also literals of the term .
Example:
If a product term subsumes a product term , then implies .
  Why?
If a sum term subsumes a sum term , then implies .
  Why?

## Slide 21: Subsumes
Theorem:
  If one term subsumes another in an expression, then the subsuming term can always be deleted from the expression without changing the function being described.
CNF:
DNF: