| http://www.ece.umd.edu/~pabshire/enee312h.htm | due Wednesday, May 8, 2002 |
| --- | --- |

- Consider the MOS differential pair with inputs Vg1 and Vg2, biased with a current I so that both transistors operate in weak inversion, as shown in the following figure:

  - Derive a transfer characteristic that expresses the difference in drain currents 
ΔI = I1-I2 as a function of the differential input voltage ΔV = Vg1-Vg2 and the bias current I.  You may neglect the Early effect and the body effect for this calculation.

  - What common scientific function does this two transistor circuit implement?

  - For a sufficiently small input signal, there is a linear relationship between the input ΔV and output ΔI.  Over what range of input signals ΔV is this linear relationship valid?  What is the transconductance ∂ΔI/∂ΔV at the midpoint of this range?

- –   8) Complete Sedra & Smith problems 5.49, 5.65, 5.81, 5.114, 6.85, 6.87, 6.88

Research Question:

One method for performing a multiplication of two analog input values is to use a translinear circuit, as explored in previous homeworks.  Another widely known and important method is the six-transistor Gilbert multiplier circuit, first described in the paper by Barrie Gilbert, “A Precise Four-Quadrant Multiplier with Subnanosecond Response,” IEEE Journal of Solid State Circuits, Vol. SC-3, pp. 365-373, Dec 1968.  Adapt the Gilbert multiplier circuit to use MOS transistors rather than BJTs, and use your results from Problem 1) above to determine the differential output current ΔI as a function of the differential input voltages ΔV1 and ΔV2.